## Slide 1
Soil Moisture Proxy Mapping & Crop Suitability Analysis
Using Remote Sensing and Machine Learning
Bidar District, Karnataka, India
Author: Sainath[23bcs115] | Course: Remote Sensing and GIS

## Slide 2
Introduction
• Soil moisture is critical for agriculture — controls germination, root growth, nutrient transport
• Field sensors are expensive & impractical for large areas
• Remote sensing offers scalable alternative using satellite imagery
• This project builds a complete geospatial pipeline:
➤ TVDI-based soil moisture proxy from MODIS data
➤ TWI from SRTM DEM for terrain moisture
➤ Multi-Criteria Evaluation for Maize suitability
➤ ML classification (RF, SVM, Gradient Boosting)
• All real satellite data — no synthetic data used

## Slide 3
Objectives
1. Acquire & preprocess multi-source remote sensing data (MODIS NDVI, LST, SRTM DEM, CHIRPS, SoilGrids)
2. Compute soil moisture proxy using TVDI triangle method + TWI
3. Perform Multi-Criteria Evaluation (MCE) for Maize crop suitability
4. Train & evaluate 3 ML classifiers for automated suitability prediction
5. Generate thematic maps and accuracy assessment reports

## Slide 4
Study Area — Bidar District
• Northernmost district of Karnataka, India
• Lat: 17.6°N – 18.3°N | Lon: 76.8°E – 77.6°E
• Deccan Plateau: 451m – 613m elevation
• Semi-arid tropical climate
• Annual rainfall: 734 – 1037 mm
• Vertisols (black cotton soil), pH ~7.5–8.0
• Major crops: Jowar, Maize, Tur, Sunflower
• Agriculture is largely rain-fed
Bounding Box: EPSG:4326 (WGS84)
Resolution: ~250 m

## Slide 5
Datasets Used
▸ NDVI
MOD13Q1 v061 | NASA AppEEARS | 250m | 23 GeoTIFFs
▸ LST
MOD11A2 v061 | NASA AppEEARS | 1 km | 45 GeoTIFFs
▸ DEM
SRTM GL1 | OpenTopography | 30m | 1 GeoTIFF
▸ Rainfall
CHIRPS v2.0 | UCSB CHRS | ~5 km | 12 files
▸ Soil pH
SoilGrids | ISRIC | 250m | 1 GeoTIFF
▸ SWI
Soil Water Index | Copernicus | 1 km | 1 GeoTIFF
Total: 163+ raw files • All real data from open-access portals • Year: 2023

## Slide 6
Methodology Overview
1. Data Preprocessing
Reproject, resample to 250m, apply scale factors, quality masking, temporal averaging
2. TWI Computation
TWI = ln(a / tan(β)) from SRTM DEM — identifies wet terrain
3. TVDI Computation
LST/NDVI triangle method — soil moisture proxy (0=wet, 1=dry)
4. Composite SMI
SMI = 0.6 × (1−TVDI) + 0.4 × TWI — combined moisture index
5. MCE Suitability
Weighted Linear Combination: SMI(40%) + Slope(20%) + Rainfall(20%) + pH(20%)
6. ML Classification
Random Forest, SVM, Gradient Boosting — trained on Copernicus SWI
7. Accuracy Assessment
Overall Accuracy, Cohen's Kappa, Confusion Matrices

## Slide 7
TVDI — Soil Moisture Proxy
TVDI = (LST_obs − LST_wet) / (LST_dry − LST_wet)
Procedure:
• Bin NDVI into 50 intervals (0.05 – 0.90)
• Extract 95th %ile LST (dry edge) per bin
• Extract 5th %ile LST (wet edge) per bin
• Fit linear regression to both edges
Fitted Edges (Bidar 2023):
Dry: LST_max = 306.7 + 5.49 × NDVI
Wet: LST_min = 299.2 + 14.04 × NDVI
TVDI range: 0.000 – 1.000

## Slide 8
TWI & Composite Soil Moisture Index
TWI = ln(a / tan(β))
• a = upstream catchment area
• β = local slope angle
• Higher TWI = flatter, wetter terrain
Composite SMI:
SMI = 0.6 × (1−TVDI) + 0.4 × TWI
• Inverts TVDI so high = wet
• Combines satellite + terrain moisture

## Slide 9
Input Data Layers
NDVI
LST
Slope
Rainfall
Soil pH
DEM

## Slide 10
MCE — Maize Suitability Results
Weighted Linear Combination:
SMI: 40% | Slope: 20% | Rainfall: 20% | pH: 20%
Suitability Distribution:
Highly Suitable (S1): 0.1%
Suitable (S2): 60.6%
Moderately Suitable (S3): 38.1%
Marginally Suitable (S4): 1.3%
Not Suitable (S5): 0.0%
Key Finding:
Over 60% of Bidar is Suitable for Maize.
Limiting factor: alkaline soil pH (~7.6)

## Slide 11
Machine Learning — 3 Algorithm Comparison
Algorithm Accuracy Kappa
Random Forest 95.28% 0.1734
SVM (RBF) 98.08% 0.0000
Gradient Boosting 97.50% 0.0465
RF Feature Importances:
Rainfall: 0.30 | LST: 0.23 | NDVI: 0.22
TWI: 0.14 | Slope: 0.11 | pH: 0.00
High accuracy but low Kappa due to
severe class imbalance (98% Class 5).
Data distribution limitation, not algorithm.

## Slide 12
ML Suitability Maps
Random Forest
SVM
Gradient Boosting

## Slide 13
Confusion Matrices
Random Forest
SVM
Gradient Boosting

## Slide 14
MCE vs ML Comparison
MCE vs ML Agreement: 1.27%
Cohen's Kappa: −0.0019
Why the disagreement?
• MCE uses expert-defined weights & thresholds
• ML learns from Copernicus SWI ground truth
• Different classification philosophies
Both approaches are complementary:
• MCE → interpretable, expert-driven
• ML → data-driven, captures non-linear patterns

## Slide 15
Limitations
1. SWI ground truth lacks georeferencing — resized to fit study area
2. SoilGrids pH had limited coverage — gaps filled with regional avg (7.6)
3. Simplified TWI using neighbourhood mean instead of D8 flow routing
4. Severe class imbalance (98% Class 5) limits ML minority-class performance
5. Temporal mismatch: MODIS 2023 vs SWI 2025 validation data

## Slide 16
Conclusion
Generated spatially continuous soil moisture proxy maps using TVDI
Over 60% of Bidar classified as Suitable for Maize (MCE)
3 ML models trained — RF, SVM, GB — all achieving ~95% accuracy
MCE provides interpretability; ML captures non-linear patterns
All analysis uses real satellite data from open-access portals
Tools: Python, rasterio, scikit-learn, matplotlib, numpy
Data: NASA, OpenTopography, ISRIC, UCSB, Copernicus

## Slide 17
References
[1] Sandholt et al. (2002) — TVDI method, Remote Sensing of Environment
[2] Beven & Kirkby (1979) — TWI, Hydrological Sciences Bulletin
[3] FAO (1976) — Framework for Land Evaluation
[4] Breiman (2001) — Random Forests, Machine Learning
[5] Congalton (1991) — Accuracy assessment, RSE
[6] Didan (2021) — MOD13Q1 NDVI product, NASA
[7] Wan et al. (2021) — MOD11A2 LST product, NASA
[8] Funk et al. (2015) — CHIRPS precipitation, Scientific Data
[9] Hengl et al. (2017) — SoilGrids250m, PLOS ONE

## Slide 18
Thank You
Questions?